## Slide 1: Lecture 18: Single Cycle Control
CSE/EEE 230
Chapter 4

## Slide 2: 5 Classic Component of Computer
CPU
Computer
Control
Datapath
Memory
Devices
Input
Output
component of the processor that performs arithmetic operations
commands datapath, memory & IO according instructions
includes internal and external memory
allows input into computer
allows output from computer

## Slide 3: Determining control
What needs to be controlled?
  Register write
  Memory read/write
  Multiplexers
What determines the control?
  Combinational logic
  Input is instruction
  Output is control signals

## Slide 4: Our Simple Control
All of the logic is combinational
Need to wait for everything to “settle down” and the correct result produced
  ALU might not produce “right answer” right away
  Can use write signals along with clock to determine when to write
Cycle time determined by length of the longest path
  critical path

## Slide 5: Data path revisited

## Slide 6: ALU Control
Input
  2 lines indicating type of instruction (ALUop)
  6 lines for function code (function code from instruction)
Output
  4 lines indicating which operation to perform
  possible 16 operations could be specified
  less are required
ALU Control Logic
ALUop
Function
code
ALU Control

## Slide 7: Adding ALU control
remember ALU op is determined by instruction opcode

## Slide 8: ALU Control
2 control lines
Determined by opcode
Examples
ALU Op | Instruction | ALU Control | Operation?
00 | lw | 0010 | 
00 | sw | 0010 | 
01 | beq | 0110 | 

## Slide 9: ALU Control for r-type
All r-type operations have the same opcode = 000000 so all r-type instructions have the same ALU Op = 10
The function code determines the ALU control
ALUOp | Instr | Function | ALU control
10 | add | 100000 | 0010
10 | sub | 100010 | 0110
10 | and | 100100 | 0000
10 | or | 100101 | 0001
10 | slt | 101010 | 0111

## Slide 10: Truth Table
ALUOp1 | ALUOp0 | F3 | F2 | F1 | F0 | Op | 
0 | 0 | X | X | X | X | 0010 | Add
0 | 1 | X | X | X | X | 0110 | Sub
1 | 0 | 0 | 0 | 0 | 0 | 0010 | Add
1 | 0 | 0 | 0 | 1 | 0 | 0110 | Sub
1 | 0 | 0 | 1 | 0 | 0 | 0000 | And
1 | 0 | 0 | 1 | 0 | 1 | 0001 | Or
1 | 0 | 1 | 0 | 1 | 0 | 0111 | Slt

## Slide 11: Logic diagram for (partial) ALU Control

## Slide 12: Controlling access to registers
32-bits
op
rs
rt
rd
sh
func
No control on read
Always reads two registers

## Slide 13: Controlling write to register
32-bits
op
rs
rt
rd
sh
func
control line RegWrite
= 1 write register
= 0 no write
data from?

## Slide 14: Setting the RegWrite control
Remember that RegWrite controls whether or not a register should change.
What should be the value of RegWrite for the following?
  r-type
  sw
  lw
  beq
  j

## Slide 15: Problem -
What registers are read?
What register is written?
What would RegWrite control line be?
000000 10001 10010 01000 00000 100000

## Slide 16: RegDst Control
What does the RegDst control?
Why is it needed?

## Slide 17: Setting the RegDst control
Remember that RegDst controls which register is written.
What should be the value of RegDst for the following?
  r-type
  sw
  lw
  beq
  j

## Slide 18: Controlling input into ALU

## Slide 19: Setting the ALUSrc control
Remember that ALUSrc determines what is the second input into that ALU.
What should be the value of ALUSrc for the following?
  r-type
  sw
  lw
  beq
  j

## Slide 20: Memory
Read data
  address 32 bits
  memread
Write data
  address 32 bits
  data 32 bits
  memwrite

## Slide 21: Setting the MemRead & MemWrite control
What should be the value of MemRead and MemWrite for the following?
  r-type
  sw
  lw
  beq
  j

## Slide 22: Controlling source of input into register

## Slide 23: Setting the MemToReg control
Remember MemToReg controls the source of the input into a register.
What should be the value of MemToReg for the following?
  r-type
  sw
  lw
  beq
  j

## Slide 24: Adding the control unit

## Slide 25: Bringing it together

## Slide 26: Logic diagram for control lines

## Slide 27: What about branching?
beq $t1, $t2, offset
steps
fetch instruction and increment PC (control?)
read $t1 and $t2 (control?)
subtract values (control?)
PC + 4 is added to sign-extended lower 16 bits of instruction (control?)
zero result from ALU is used to determine value in PC (control?)

## Slide 28: Control with branch

## Slide 29: What about jump?
opcode = 000010
remainder of instruction is address
  26 bits
need to
  shift bits 2 to left
  replace lower 28 bits of PC
what control needs to be done?
  can shifting always be done?
  where does decision need to be done?

## Slide 30: “complete” picture

## Slide 31: Performance Issues
Longest delay determines clock period
  Critical path: load instruction
  Instruction memory  register file  ALU  data memory  register file
Not feasible to vary period for different instructions
Violates design principle
  Making the common case fast